Kenwood TM-D710A (K Type) Profile Settings

Items highlighted like THIS are values that have been changed to something other than the default.
Items highlighted like THIS are values that are currently awaiting verification.

AUDIO	PM 0 (PM OFF)	PM 1	PM 2	PM 3	PM 4	PM 5
000 KEY BEEP	OFF	OFF	OFF	OFF	OFF	OFF
003 ANNOUNCE	MANUAL	MANUAL	MANUAL	MANUAL	MANUAL	MANUAL

TX/RX	PM 0	PM 1	PM 2	PM 3	PM 4	PM 5
100 PROGRAMMABLE VFO *	144- 148 MHz	144- 148 MHz	144- 148 MHz	144- 148 MHz	144- 148 MHz	144- 148 MHz

* menu item not visible unless radio is in the appropriate mode

REPEATER	PM 0 (PM OFF)	PM 1	PM 2	PM 3	PM 4	PM 5
405 REPEATER ID	VA3DGN	N/A	N/A	N/A	N/A	N/A
406 REPEATER ID TX	MORSE	N/A	N/A	N/A	N/A	N/A

AUX	PM 0 (PM OFF)	PM 1	PM 2	PM 3	PM 4	PM 5
500 POWER ON MESSAGE	Fixed	Xband	Digi	CNCycle	RLCT	Mobile
503 BACKLIGHT COLOR	GREEN	GREEN	GREEN	GREEN	GREEN	GREEN
508 PANEL PF2	MONITOR	MONITOR	MONITOR	MONITOR	MONITOR	MONITOR
510 MIC PF2 (MR)	ENTER	ENTER	ENTER	ENTER	ENTER	ENTER
521 AUTO PM STORE *	N/A	OFF	OFF	OFF	OFF	OFF
526 TIME ZONE	-04:00	-04:00	-04:00	-04:00	-04:00	-04:00
529 INT. DATA BAND (PACKET)	B-BAND	B-BAND	B-BAND	B-BAND	B-BAND	B-BAND

* menu item not visible unless radio is in the appropriate mode

APRS	PM 0 (PM OFF)	PM 1	PM 2	PM 3	PM 4	PM 5
600 BASIC SETTINGS	MY CALLSIGN : VA3DGN-9 / BEACON TYPE : APRS	MY CALLSIGN : VA3DGN-9 / BEACON TYPE : APRS	MY CALLSIGN : VA3DGN-9 / BEACON TYPE : APRS	MY CALLSIGN : VA3DGN-9 / BEACON TYPE : APRS	MY CALLSIGN : VA3DGN-9 / BEACON TYPE : APRS	MY CALLSIGN : VA3DGN-9 / BEACON TYPE : APRS
601 INTERNAL TNC	DATA BAND : B-BAND / DATA SPEED : 1200 bps / DCD SENSE : D or RxD BAND / TX DELAY : 200 ms	DATA BAND : B-BAND / DATA SPEED : 1200 bps / DCD SENSE : D or RxD BAND / TX DELAY : 200 ms	DATA BAND : B-BAND / DATA SPEED : 1200 bps / DCD SENSE : BOTH BANDS / TX DELAY : 200 ms	DATA BAND : B-BAND / DATA SPEED : 1200 bps / DCD SENSE : BOTH BANDS / TX DELAY : 200 ms	DATA BAND : B-BAND / DATA SPEED : 1200 bps / DCD SENSE : D or RxD BAND / TX DELAY : 200 ms	DATA BAND : B-BAND / DATA SPEED : 1200 bps / DCD SENSE : D or RxD BAND / TX DELAY : 200 ms
602 GPS PORT	BAUD RATE : 4800 bps / INPUT : GPS / OUTPUT : OFF	BAUD RATE : 4800 bps / INPUT : GPS / OUTPUT : OFF	BAUD RATE : 4800 bps / INPUT : GPS / OUTPUT : OFF	BAUD RATE : 4800 bps / INPUT : GPS / OUTPUT : OFF	BAUD RATE : 4800 bps / INPUT : GPS / OUTPUT : OFF	BAUD RATE : 4800 bps / INPUT : GPS / OUTPUT : OFF
607 POSITION COMMENT	Off Duty	Special	Special	In Service	In Service	Enroute
608 STATUS TEXT	*1 TEXT : / TX RATE : OFF	*1 TEXT : / TX RATE : OFF	*2 TEXT : Fill-in digipeter / TX RATE : 1/1	*3 TEXT : Fill-in digipeter / TX RATE : 1/1	*4 TEXT : SAG1 / TX RATE : 1/1	*5 TEXT : [Freq MHz] / TX RATE : 1/1
609 PACKET FILTER	POSITION LIMIT : OFF / TYPE : *WEATHER *DIGI / *MOBILE *OBJECT / *NAVITRA *OTHERS	POSITION LIMIT : OFF / TYPE : *WEATHER *DIGI / *MOBILE *OBJECT / *NAVITRA *OTHERS	POSITION LIMIT : OFF / TYPE : *WEATHER *DIGI / *MOBILE *OBJECT / *NAVITRA *OTHERS	POSITION LIMIT : 10 / TYPE : WEATHER DIGI / *MOBILE OBJECT / NAVITRA OTHERS	POSITION LIMIT : OFF / TYPE : *WEATHER *DIGI / *MOBILE *OBJECT / *NAVITRA *OTHERS	POSITION LIMIT : OFF / TYPE : *WEATHER *DIGI / *MOBILE *OBJECT / *NAVITRA *OTHERS
610 STATION ICON	Car SYMBOL : > / TABLE : /	Car SYMBOL : > / TABLE : /	Digipeter SYMBOL : # / TABLE : /	Digipeter SYMBOL : # / TABLE : /	Car SYMBOL : > / TABLE : /	Car SYMBOL : > / TABLE : /
611 BEACON TX ALGORITHM	METHOD : MANUAL / INITIAL INTERVAL : 3 min / DECAY ALGORITHM : ON / PROPORTIONAL PATHING : ON	METHOD : MANUAL / INITIAL INTERVAL : 3 min / DECAY ALGORITHM : ON / PROPORTIONAL PATHING : ON	METHOD : SmartBeaconing / INITIAL INTERVAL : 3 min / DECAY ALGORITHM : ON / PROPORTIONAL PATHING : ON	METHOD : SmartBeaconing / INITIAL INTERVAL : 3 min / DECAY ALGORITHM : ON / PROPORTIONAL PATHING : ON	METHOD : SmartBeaconing / INITIAL INTERVAL : 3 min / DECAY ALGORITHM : ON / PROPORTIONAL PATHING : ON	METHOD : SmartBeaconing / INITIAL INTERVAL : 3 min / DECAY ALGORITHM : ON / PROPORTIONAL PATHING : ON
612 PACKET PATH	TYPE : *New-N PARADIGM / WIDE1-1 : ON / TOTAL HOPS : 2 / PATH IS VIA : WIDE1-1,WIDE2-1	TYPE : *New-N PARADIGM / WIDE1-1 : ON / TOTAL HOPS : 2 / PATH IS VIA : WIDE1-1,WIDE2-1	TYPE : *New-N PARADIGM / WIDE1-1 : ON / TOTAL HOPS : 2 / PATH IS VIA : WIDE1-1,WIDE2-1	TYPE : *New-N PARADIGM / WIDE1-1 : ON / TOTAL HOPS : 2 / PATH IS VIA : CN,WIDE1-1how do I set this?	TYPE : *New-N PARADIGM / WIDE1-1 : ON / TOTAL HOPS : 2 / PATH IS VIA : WIDE1-1,WIDE2-1	TYPE : *New-N PARADIGM / WIDE1-1 : ON / TOTAL HOPS : 2 / PATH IS VIA : WIDE1-1,WIDE2-1
616 DIGIPEAT (MY CALL)	DIGIPEAT : OFF	DIGIPEAT : OFF	DIGIPEAT : OFF	DIGIPEAT : OFF	DIGIPEAT : OFF	DIGIPEAT : OFF
618 UIDIGI	UIDIGI : OFF / ALIASES :	UIDIGI : OFF / ALIASES :	UIDIGI : ON / ALIASES :	UIDIGI : ON / ALIASES : CN	UIDIGI : OFF / ALIASES :	UIDIGI : OFF / ALIASES :
624 SOUND	RX BEEP : MESSAGE ONLY / TX BEEP : OFF / SPECIAL CALL : / APRS VOICE : ON	RX BEEP : MESSAGE ONLY / TX BEEP : OFF / SPECIAL CALL : / APRS VOICE : ON	RX BEEP : MESSAGE ONLY / TX BEEP : OFF / SPECIAL CALL : / APRS VOICE : ON	RX BEEP : MESSAGE ONLY / TX BEEP : OFF / SPECIAL CALL : / APRS VOICE : ON	RX BEEP : MESSAGE ONLY / TX BEEP : OFF / SPECIAL CALL : / APRS VOICE : ON	RX BEEP : MESSAGE ONLY / TX BEEP : OFF / SPECIAL CALL : / APRS VOICE : ON
625 INTERRUPT DISPLAY	DISPLAY AREA : OFF / AUTO BRIGHTNESS : ON / CHANGE COLOR : ON / INTERRUPT TIME : 10 sec	DISPLAY AREA : OFF / AUTO BRIGHTNESS : ON / CHANGE COLOR : ON / INTERRUPT TIME : 10 sec	DISPLAY AREA : OFF / AUTO BRIGHTNESS : ON / CHANGE COLOR : ON / INTERRUPT TIME : 10 sec	DISPLAY AREA : OFF / AUTO BRIGHTNESS : ON / CHANGE COLOR : ON / INTERRUPT TIME : 10 sec	DISPLAY AREA : OFF / AUTO BRIGHTNESS : ON / CHANGE COLOR : ON / INTERRUPT TIME : 10 sec	DISPLAY AREA : OFF / AUTO BRIGHTNESS : ON / CHANGE COLOR : ON / INTERRUPT TIME : 10 sec
626 DISPLAY UNIT 1	SPEED, DISTANCE : km/h, km / ALTITUDE, RAIN : m, mm / TEMPERATURE : °C	SPEED, DISTANCE : km/h, km / ALTITUDE, RAIN : m, mm / TEMPERATURE : °C	SPEED, DISTANCE : km/h, km / ALTITUDE, RAIN : m, mm / TEMPERATURE : °C	SPEED, DISTANCE : km/h, km / ALTITUDE, RAIN : m, mm / TEMPERATURE : °C	SPEED, DISTANCE : km/h, km / ALTITUDE, RAIN : m, mm / TEMPERATURE : °C	SPEED, DISTANCE : km/h, km / ALTITUDE, RAIN : m, mm / TEMPERATURE : °C

MAIN	PM 0 (PM OFF)	PM 1	PM 2	PM 3	PM 4	PM 5
A-BAND	MEMORY 1, SELECTED	MEMORY 1, SELECTED	MEMORY 1, SELECTED	MEMORY 1, SELECTED	MEMORY 1, SELECTED	MEMORY 1, SELECTED
B-BAND	MEMORY 1	MEMORY 1	MEMORY 88 (APRS)	MEMORY 88 (APRS)	MEMORY 88 (APRS)	MEMORY 88 (APRS)
TNC	OFF	OFF	APRS12	APRS12	APRS12	APRS12

AUDIO	DEFAULT	VALUES/NOTES
000 KEY BEEP	ON	OFF, ON
001 BEEP VOLUME	LEVEL 5	LEVEL 1, LEVEL 2, LEVEL 3, LEVEL 4, LEVEL 5, LEVEL 6, LEVEL 7
002 EXT. SPEAKER	MODE 1	MODE 1, MODE 2
003 ANNOUNCE	AUTO	AUTO, MANUAL, OFF
004 ANNOUNCE LANGUAGE	ENGLISH	ENGLISH, JAPANESE
005 ANNOUNCE VOLUME	LEVEL 3	LEVEL 1, LEVEL 2, LEVEL 3, LEVEL 4, LEVEL 5, LEVEL 6, LEVEL 7
006 ANNOUNCE SPEED	SPEED 1	SPEED 0, SPEED 1, SPEED 2, SPEED 3, SPEED 4
007 PLAYBACK REPEAT	OFF	OFF, ON
008 PLAYBACK INTERVAL	10 s	0 to 60 s
009 CONTINUOUS RECORDING	OFF	OFF, ON

TX/RX	DEFAULT	VALUES/NOTES
100 PROGRAMMABLE VFO *	136- 199 MHz
101 STEP *	5.0 kHz	5.0, 6.25, 8.33 (118 MHz band only), 10.0, 12.5, 15.0, 20.0, 25.0, 30.0, 50.0, 100.0 kHz
102 MODULATION	FM
103 VHF AIP	OFF	OFF, ON
104 UHF AIP	OFF	OFF, ON
105 S-METER SQUELCH	OFF	OFF, ON
106 S-METER SQL HANGUP TIME	OFF	125 ms, 250 ms, 500 ms, OFF
107 MUTE HANGUP TIME	OFF	125 ms, 250 ms, 500 ms, 750 ms, 1000 ms, OFF
108 BEAT SHIFT	OFF	OFF, ON
109 TOT	10 min	3 min, 5 min, 10 min
110 WEATHER ALERT	OFF	OFF, ON
111 MICROPHONE SENSITIVITY	MEDIUM	HIGH, LOW, MEDIUM

* menu item not visible unless radio is in the appropriate mode

MEMORY	DEFAULT	VALUES/NOTES
200 MEMORY NAME		Up to 8 characters
201 RECALL METHOD	ALL BANDS	ALL BANDS, CURRENT
202 LOCKOUT	ON	OFF, ON
203 GROUP LINK		Up to 10 digits
204 EchoLink MEMORY		Up to 8 characters for EchoLink memory name; Up to 8 digits for DTMF code
205 EchoLink SPEED	FAST	FAST, SLOW

DTMF	DEFAULT	VALUES/NOTES
300 DTMF HOLD	OFF	OFF, ON
301 DTMF MEMORY		Up to 8 characters for DTMF memory name; Up to 16 digits for DTMF code
302 DTMF SPEED	FAST	FAST, SLOW
303 DTMF PAUSE	500 ms	100 ms, 250 ms, 500 ms, 750 ms, 1000 ms, 1500 ms, 2000 ms
304 DTMF KEY LOCK	OFF	OFF, ON

REPEATER	DEFAULT	VALUES/NOTES
400 OFFSET FREQUENCY	0.600 MHz
401 AUTO REPEATER OFFSET	ON	OFF, ON
402 1750 TX HOLD	OFF	OFF, ON
403 REPEATER MODE	CROSS BAND	CROSS BAND, LOCKED TX: A-BAND, LOCKED TX: B-BAND
404 REPEATER TX HOLD	OFF	OFF, ON
405 REPEATER ID	NOCALL	Up to 12 characters
406 REPEATER ID TX	OFF	MORSE, OFF, VOICE

AUX	DEFAULT	VALUES/NOTES
500 POWER ON MESSAGE	HELLO !!	Up to 8 characters
501 BRIGHTNESS	LEVEL 8	LEVEL 1, LEVEL 2, LEVEL 3, LEVEL 4, LEVEL 5, LEVEL 6, LEVEL 7, LEVEL 8, OFF
502 AUTO BRIGHTNESS	OFF	OFF, ON
503 BACKLIGHT COLOR	AMBER	AMBER, GREEN
504 CONTRAST	LEVEL 8	LEVEL 1, LEVEL 2, LEVEL 3, LEVEL 4, LEVEL 5, LEVEL 6, LEVEL 7, LEVEL 8, LEVEL 9, LEVEL 10, LEVEL 11, LEVEL 12, LEVEL 13, LEVEL 14, LEVEL 15, LEVEL 16
505 DISPLAY REVERSE MODE	POSITIVE	NEGATIVE, POSITIVE
507 PANEL PF1	WX CH	1750, CTRL, DUAL, DX, FRQ.BAND, GROUP UP, M>V, MENU, MONITOR, MUTE, SHIFT, VGS, VOICE, WX CH
508 PANEL PF2	CTRL	1750, CTRL, DUAL, DX, FRQ.BAND, GROUP UP, M>V, MENU, MONITOR, MUTE, SHIFT, VGS, VOICE, WX CH
509 MIC PF1 (PF)	A/B	1750, A/B, BEACON, CALL, CTRL, DUAL, DX, ENTER, FRQ.BAND, GROUP UP, LOCK, LOW, M.LIST, M>V, MENU, MHz, MONITOR, MR, MSG.NEW, MUTE, P.MONI, POS, REPLY, REV, S.LIST, SHIFT, TONE, VFO, VGS, VOICE, WX CH
510 MIC PF2 (MR)	MR	1750, A/B, BEACON, CALL, CTRL, DUAL, DX, ENTER, FRQ.BAND, GROUP UP, LOCK, LOW, M.LIST, M>V, MENU, MHz, MONITOR, MR, MSG.NEW, MUTE, P.MONI, POS, REPLY, REV, S.LIST, SHIFT, TONE, VFO, VGS, VOICE, WX CH
511 MIC PF3 (VFO)	VFO	1750, A/B, BEACON, CALL, CTRL, DUAL, DX, ENTER, FRQ.BAND, GROUP UP, LOCK, LOW, M.LIST, M>V, MENU, MHz, MONITOR, MR, MSG.NEW, MUTE, P.MONI, POS, REPLY, REV, S.LIST, SHIFT, TONE, VFO, VGS, VOICE, WX CH
512 MIC PF4 (CALL)	CALL	1750, A/B, BEACON, CALL, CTRL, DUAL, DX, ENTER, FRQ.BAND, GROUP UP, LOCK, LOW, M.LIST, M>V, MENU, MHz, MONITOR, MR, MSG.NEW, MUTE, P.MONI, POS, REPLY, REV, S.LIST, SHIFT, TONE, VFO, VGS, VOICE, WX CH
513 MIC KEY LOCK	OFF	OFF, ON
514 SCAN RESUME	TIME	CARRIER, TIME, SEEK
515 VISUAL SCAN	MODE 2 : 61ch	MODE 1 : 31ch, MODE 2 : 61ch, MODE 3 : 91ch, MODE 4 : 181ch
516 APO	OFF	30, 60, 90, 120, 180, OFF; Measured in minutes
517 EXT. DATA BAND	B-BAND	A-BAND, B-BAND, RX : A-BAND TX : B-BAND, TX : A-BAND RX : B-BAND
518 EXT. DATA SPEED	1200 bps	1200 bps, 9600 bps
519 PC PORT BAUDRATE	9600 bps	9600 bps, 19200 bps, 38400 bps, 57600 bps
520 SQC SOURCE	BUSY or TX	BUSY, BUSY or TX, OFF, SQL, SQL OR TX, TX
521 AUTO PM STORE *	ON	OFF, ON
522 REMOTE ID	000	000 to 999
523 REMOTE ANSWER BACK	ON	OFF, ON
524 DATE
525 TIME
526 TIME ZONE	UTC	UTC + 14:00 to UTC -14:00 in 0:15 increments
527 DISPLAY PARTITION BAR	ON	OFF, ON
528 COM PORT BAUDRATE	9600 bps	9600 bps, 19200 bps, 38400 bps, 57600 bps
529 INT. DATA BAND (PACKET)	A-BAND	A-BAND, B-BAND, RX : A-BAND TX : B-BAND, TX : A-BAND RX : B-BAND

* menu item not visible unless radio is in the appropriate mode

APRS	DEFAULT	VALUES/NOTES
600 BASIC SETTINGS	MY CALLSIGN : NOCALL / BEACON TYPE : APRS	Up to 9 characters / APRS, NAVITRA
601 INTERNAL TNC	DATA BAND : A-BAND / DATA SPEED : 1200 bps / DCD SENSE : D or RxD BAND / TX DELAY : 200 ms	A-BAND, B-BAND, RX : A-BAND TX : B-BAND, TX : A-BAND RX : B-BAND / 1200 bps, 9600 bps / BOTH BAND, D or RxD BAND, IGNORE DCD / 100 ms, 150 ms, 200 ms, 300 ms, 400 ms, 500 ms, 750 ms, 1000 ms
602 GPS PORT	BAUD RATE : 4800 bps / INPUT : OFF / OUTPUT : OFF	2400 bps, 4800 bps, 9600 bps / GPS, OFF, WEATHER(Davis), WEATHER(PeetBros) / DGPS, OFF, WAYPOINT
603 WAYPOINT	FORMAT : NMEA / NAME : 6-CHAR / OUTPUT : ALL	KENWOOD, MAGELLAN, NMEA / 6-CHAR, 7-CHAR, 8-CHAR, 9-CHAR / ALL, FILTERED, LOCAL
604 COM PORT	OUTPUT : OFF	OFF, ON
605 MY POSITION	*1 NAME : / LATUTUDE : N 00°00.00' / LONGITUDE : W 000°00.00' / JJ00AA	Up to ? characters
606 BEACON INFORMATION	SPEED : ON / ALTITUDE : ON / POSITION AMBIGUITY : OFF	OFF, ON / OFF, ON / 1-DIGIT, 2-DIGIT, 3-DIGIT, 4-DIGIT, OFF
607 POSITION COMMENT	Off Duty	Committed, CUSTOM 0, CUSTOM 1, CUSTOM 2, CUSTOM 3, CUSTOM 4, CUSTOM 5, CUSTOM 6, EMERGENCY!, Enroute, In Service, Off Duty, PRIORITY, Returning, Special
608 STATUS TEXT	*1 TEXT : / TX RATE : OFF	Up to ? characters / 1/1, 1/2, 1/3, 1/4, 1/5, 1/6, 1/7, 1/8, OFF
609 PACKET FILTER	POSITION LIMIT : OFF / TYPE : *WEATHER *DIGI / *MOBILE *OBJECT / *NAVITRA *OTHERS	?
610 STATION ICON	KENWOOD SYMBOL : K / TABLE : \
611 BEACON TX ALGORITHM	METHOD : MANUAL / INITIAL INTERVAL : 3 min / DECAY ALGORITHM : ON / PROPORTIONAL PATHING : ON	AUTO, MANUAL, PTT, SmartBeaconing / 0.2 min, 0.5 min, 1 min, 3 min, 5 min, 10 min, 20 min, 30 min, 60 min / OFF, ON / OFF, ON
612 PACKET PATH	TYPE : *New-N PARADIGM / WIDE1-1 : ON / TOTAL HOPS : 2 / PATH IS VIA : WIDE1-1,WIDE2-1	New-N PARADIGM, OTHERS, RELAY PARADIGM, STATE/SECTION/REGION / OFF, ON / ? / ?
613 NETWORK	*APRS / ALTNET :	APRS(APK102), ALTNET / Up to 9 characters
614 VOICE ALERT	VOICE ALERT : OFF / CTCSS FREQUENCY : 100.0 Hz	OFF, ON
615 WEATHER STATION	TX : OFF / TX INTERVAL : 5 min	OFF, ON / 5 min, 10 min, 30 min
616 DIGIPEAT (MY CALL)	DIGIPEAT : OFF	OFF, ON
617 UICHECK	TIME : 28 sec	0 to 250 sec
618 UIDIGI	UIDIGI : OFF / ALIASES :	OFF, ON / Up to 39? characters
619 UIFLOOD	UIFLOOD : OFF / ALIAS : / SUBSTITUTION : ID	OFF, ON / Up to 5 characters / FIRST, ID, NOID
620 UITRACE	UITRACE : ON / ALIAS : TEMP	OFF, ON / Up to 5 characters
621 USER PHRASES	1: / 2: / 3: / 4:	Up to 32 characters / Up to 32 characters / Up to 32 characters / Up to 32 characters
622 AUTO MESSAGE REPLY	REPLY : OFF / TEXT : / REPLY TO : *	OFF, ON / Up to 50 characters / Up to 9 characters
623 GROUP FILTERING	MESSAGE : ALL,QST,CQ,KWD / BLN :	Up to 59 characters / Up to 20 characters
624 SOUND	RX BEEP : ALL / TX BEEP : OFF / SPECIAL CALL : / APRS VOICE : ON	ALL, ALL NEW, MESSAGE ONLY, MINE, OFF / OFF, ON / Up to 9 characters / OFF, ON
625 INTERRUPT DISPLAY	DISPLAY AREA : ENTIRE ALWAYS / AUTO BRIGHTNESS : ON / CHANGE COLOR : ON / INTERRUPT TIME : 10 sec	HALF, ENTIRE, ENTIRE ALWAYS, OFF / OFF, ON / OFF, ON / 3 sec, 5 sec, 10 sec, INFINITE
626 DISPLAY UNIT 1	SPEED, DISTANCE : mi/h, mile / ALTITUDE, RAIN : feet, inch / TEMPERATURE : °F	'mi/h, mile', 'km/h, km', 'knots, nm' / 'feet, inch', 'm, mm' / °F, °C
627 DISPLAY UNIT 2	POSITION : dd°mm.mm' / GRID FORMAT : MAIDENHEAD GRID	dd°mm.mm', dd°mm' ss.s'' / MAIDENHEAD GRID, SAR GRID (CELL), SAR GRID (CONV)
628 NAVITRA GROUP	GROUP MODE : OFF / GROUP CODE : 000	OFF, ON / Up to 3 characters
629 NAVITRA MESSAGE	*1:	Up to 20 characters
630 SMARTBEACONING 1	LOW SPEED : 5 / HIGH SPEED : 70 / SLOW RATE : 30 min / FAST RATE : 120 sec	2 to 30 / 2 to 90 / 1 to 100 min / 10 to 180 sec
631 SMARTBEACONING 2	TURN ANGLE : 28 deg / TURN SLOPE : 26 (10deg/speed) / TURN TIME : 30 sec	5 to 90 deg / 1 to 255 (10deg/speed) / 5 to 180 sec

SKY CMD	DEFAULT	VALUES/NOTES
700 COMMANDER CALLSIGN	NOCALL	Up to 9 characters
701 TRANSPORTER CALLSIGN	NOCALL	Up to 9 characters
702 TONE FREQUENCY	88.5 Hz
703 SKY COMMAND	OFF	COMMANDER, OFF, TRANSPORTER

AUX 2	DEFAULT	VALUES/NOTES
998 POWER ON PASSWORD	OFF	OFF, ON
999 RESET	VFO RESET	FULL RESET, PARTIAL RESET, PM RESET, VFO RESET